## Slide 1
A roadmap to energy efficient community-different approaches, the same aim
Thomas Duwe

## Slide 2
seven communities from four countries:
Duplek (Slovenia)
Prusice (Poland)
Blansko and Opava (Czech Republic)
Niestetal, Baunatal, Cölbe (Germany)
5.2.1 Analysis of energy consumption data in communities
Value | Inh. | Inh./km² | GWh | t CO2 | GWh/inh. | t CO2/inh.
Min | 6,651 | 60 | 36 | 12,026 | 5,428 | 1.81
Max | 48,456 | 1,148 | 730 | 344,068 | 17,404 | 6.38
Median | 10,572 | 478 | 184 | 59,082 | 13,878 | 4.08

## Slide 3
Small, next to big city, low heating demand, little industry
Duplek - 6,651 inh. - 166 inh./km²
Sector | end energy | CO2 | End energy per person | CO2 per person
heat | 21.5 GWh | 4,361 t/a | 3,233 kWh | 0.66 t/a/p
electricity | 13.5 GWh | 7,125 t/a | 2,030 kWh | 1.07 t/a/p
total | 36.1 GWh | 12,026 t/a | 5,428 kWh | 1.81 t/a/p
Sector | Potential | Potential | CO2- savings | CO2- savings
heat | 13 GWh | 60 % | 2,637 t/a | 60 %
electricity | 3 GWh | 22 % | 1,583 t/a | 22 %
total | 16 GWh | 46 % | 4.220 t/a | 37 %

## Slide 4
Rural area
No gas grid - Wood and oil for heating
Very low electricity demand
High heat demand per m²
Prusice - 9,377 inh. - 60 inh./km²
Sector | end energy | CO2 | End energy per person | CO2 per person
heat | 90.3 GWh | 17,400 t/a | 9,630 kWh | 1.86 t/a/p
electricity | 12.9 GWh | 15,300 t/a | 1,376 kWh | 1.63 t/a/p
total | 103 GWh | 32,700 t/a | 11,006 kWh | 3.49 t/a/p
Sector | Potential | Potential | CO2- savings | CO2- savings
heat | 59 GWh | 65 % | 11,292 t/a | 65 %
electricity | 2 GWh | 16 % | 2,372 t/a | 16 %
total | 61 GWh | 59 % | 13,664 t/a | 43 %

## Slide 5
Opava - 58,456 inh. - 650 inh./km²
Sector | end energy | CO2 | End energy per person | CO2 per person
heat | 473 GWh | 77,206 t/a | 8,092 kWh | 1.32 t/a/p
electricity | 257 GWh | 266,862 t/a | 4,396 kWh | 4.57 t/a/p
total | 730 GWh | 344,068 t/a | 12,488 kWh | 5.89 t/a/p
Big industry
Gas and heating network
Sector | Potential | Potential | CO2- savings | CO2- savings
heat | 189 GWh | 40 % | 41,623 t/a | 40 %
electricity | 44 GWh | 17 % | 52,957 t/a | 17 %
total | 233 GWh | 32 % | 94,580 t/a | 22 %

## Slide 6
Very dens city
Huge gas consumption in industry – lower % saving potential
Heating network and gas for heating!
Emission saving through RES!!
Blansko - 21,000 inh. - 1,148 inh./km²
Sector | end energy | CO2 | End energy per person | CO2 per person
heat | 268 GWh | 56,000 t/a | 12,762 kWh | 2.67 t/a/p
electricity | 68 GWh | 78,000 t/a | 3,238 kWh | 3.71 t/a/p
total | 336 GWh | 134,000 t/a | 16,000 kWh | 6.38 t/a/p
Sector | Potential | Potential | CO2- savings | CO2- savings
heat | 84 GWh | 31 % | 17,552 t/a | 31 %
electricity | 14 GWh | 21 % | 16,059 t/a | 21 %
total | 98 GWh | 29 % | 33,611 t/a | 25 %

## Slide 7
Niestetal - 10,572 inh. - 478 inh./km²
Sector | end energy | CO2 | End energy per person | CO2 per person
heat | 143 GWh | 39,347 t/a | 13,526 kWh | 3.72 t/a/p
electricity | 41 GWh | 19,735 t/a | 3,878 kWh | 1.87 t/a/p
total | 184 GWh | 59,082 t/a | 17,404 kWh | 5.59 t/a/p
Small city next to Kassel
Highest per capita consumption – highest saving potential
Saving potential through less m² per person!!
Sector | Potential | Potential | CO2- savings | CO2- savings
heat | 103 GWh | 72 % | 28,341 t/a | 72 %
electricity | 8 GWh | 20 % | 3,851 t/a | 20 %
total | 111 GWh | 60 % | 32,192 t/a | 54 %

## Slide 8
Baunatal - 27,747 inh. - 728 inh./km²
Sector | end energy | CO2 | End energy per person | CO2 per person
heat | 268 GWh | 56,000 t/a | 12,762 kWh | 2.67 t/a/p
electricity | 68 GWh | 78,000 t/a | 3,238 kWh | 3.71 t/a/p
total | 336 GWh | 134,000 t/a | 16,000 kWh | 6.38 t/a/p
City next to Kassel
VW production facility not included!
 heating demand per person is higher in Germany!
Sector | Potential | Potential | CO2- savings | CO2- savings
heat | 211 GWh | 67 % | 46,870 t/a | 67 %
electricity | 17 GWh | 19 % | 8,336 t/a | 19 %
total | 228 GWh | 57 % | 55.206 t/a | 49 %

## Slide 9
Cölbe - 7,047 inh. - 264 inh./km²
Sector | end energy | CO2 | End energy per person | CO2 per person
heat | 72.6 GWh | 20,400 t/a | 10,302 kWh | 2.89 t/a/p
electricity | 25.2 GWh | 8,250 t/a | 3,576 kWh | 1.17 t/a/p
total | 97.8 GWh | 28,650 t/a | 13,878 kWh | 4.07 t/a/p
more rural community
RES district heating in Schönstadt
Sector | Potential | Potential | CO2- savings | CO2- savings
heat | 56 GWh | 68 % | 15,848 t/a | 68 %
electricity | 5 GWh | 20 % | 1,637 t/a | 20 %
total | 61 GWh | 63 % | 17.485 t/a | 54 %

## Slide 10
Mobility main issue after heating
Next to Marburg, shuttle traffic, distance 12 km
Also: railway station: 6km
Ideal for E-bikes!
Need for bike boxes against theft and whether
App for reserving and checking availability
Can build on carsharing community and service
Different Approaches and Measures - Cölbe
www.coelbe.de

## Slide 11
Aim for CO2 neutrality in 2035
Need for building renovation: 3% or more
Acutally achieved through funding programm (ended)
Two quarter concepts. Goal: 5-6% by
  Quarter manager will actively consulate citizens/house owners
  Offer: contract with renovation roadmap with 5-6% grant
Niestetal
www.niestetal.de

## Slide 12
Quarter concepts
  Extension district heating
  Demografic affairs
  Street renovation
  E-mobility
  Change of housing association – chance for new impuls
    Barrier free
    Tailoring of the apartments
LED in street lighting, 10-20% per year
Baunatal
www.baunatal.de

## Slide 13
Recommended actions:
  Energetic renovationof buildings
  Change of behaviour
  exchange of devices
  Exchange of old heating systems with more efficent ones
  Subsidies for RES plants
Prusice
www.prusice.pl

## Slide 14
Advanced Strategic Energy Planning & Energy management
  EPC and ESKO projects
  Energy project buffer
  Smart Meetering
E-mobility
  Public transport fully electrical
  City Police
Statutory City of Opava

## Slide 15
Projects Examples
  PV system on primary schools and public buildings
    Pilot project „Šrámkova primary school“
  Biomass production
    Cultivation of fast-growing trees on City grounds
    Use of biomass from city parks and green areas
  Complex building renovations
    Mainly Primary schools
Statutory City of Opava

## Slide 16
Duplek
Sector households:
  Largest Energy efficiency/savings potential
  Good potential for energy efficiency cooperatives, local/ national incentives;
Sector industry: undeveloped – largest potentials in electricity;
Public sector: highest potential in public lighting and thermo-modernization;
Traffic: next to biggest city of the region – Maribor; advocating use of sustainable mobility solutions (e-mobility, mobility on demand, alternative transport modes);
www.duplek.si

## Slide 17
Thank you very much for attention!